## Slide 1: SEAM AI
Applied Geoscience Hackathon
Application Form
Due 1 March 2021

## Slide 2: TEAM CONTACT INFORMATION
Team Name: MathWorks
Name of Team Lead for Communications: Samvith Rao
Email for All Event Communications: Samvith.Rao@MathWorks.com
Instructions:
In the box below, please provide a team name and contact information for the team member who will handle communications regarding the event.

## Slide 3: understanding of Problem Statement
Quantitative facies classification is the key to understanding seismic data to evaluate important reservoir properties. During the past several years, the size of seismic volumes has piled up to the extent that it is challenging for geoscientists to manually examine every seismic volume to classify the facies. This is where new methodologies such as deep learning fit in. They help automate these tasks. However so far, this approach has not been a runaway success.
The reason is twofold –
During the initial rounds, the most important pixels to identify are faults and horizons. Most algorithms have trouble segmenting pixels at the boundaries of these prominent geologic structures.
Lack of appropriate metrics. While there are some quantitative measures drawn from the classic image processing domain (e.g. IOU), these are not ‘geologically informed’. An aim of this competetion is to test new metrics that indicate the true quality of fault or horizon extraction.
INSTRUCTIONS:
In the box below—and on following slides (if desired)—provide a narrative with your understanding of the problem statement and goals of the Applied Geoscience Hackathon. Use as many slides as you wish but try not to just copy from the information provided.

## Slide 4: Proposed solution
INSTRUCTIONS:
In the box below, provide a description of your team’s proposed approach to the problem. This is just a starting proposal. If selected, your team will work with mentors and with input from other teams to further develop and implement your approach. Use as many slides as you wish.
Executive Summary: Our proposed method consists of upscaling the seismic images before feeding them to the deep learning model. We will use the wavelet transform as an upscaling technique. Wavelet based multiresolution analysis is a powerful framework for extracting relevant features from complex signals without adding any spatial distortions or artifacts. These features will be paired with AI models for classification.
To illustrate its feasibility and effectiveness, the proposed method was applied to seismic data from Antarctica, and we could clearly identify the interfaces between ice sheet and bed rock. The results have demonstrated that wavelets combined with deep learning can distinguish among different facies, helping the interpreter to process new seismic images. There are two main advantages of this method over using only deep learning:
Improved resolution at boundaries of geologic structures leads to better training data for the deep learning model and hence better classification achieving mean accuracy of 95%
Reduction in the amount of labeled data needed for training and increasing the productivity of the interpreter by ~10x

## Slide 5: Proposed Workflow – Segmentation of images with wavelets & CNNs
Train Deep Networks
Test Network
Signal Preprocessing with Wavelets
Seismic Data
Segmented Seismic Data
Deploy network on NVIDIA GPU

## Slide 6: CASE STUDY

## Slide 7: the proposed workflow has already been demonstrated successfully on polar ice sheets
Icesheets
Bedrock

## Slide 8: Radar data of Antarctic ice sheets are analogous to seismic data

## Slide 9: Case Study Data
Season 2012 2009
Operating frequency 180-210 MHz 140-160 MHz
Pulse Duration 1,3,10 s 1,3,10 s
Sampling freq 111.11MHz 120 MHz
Max Tx channels 8 6
Max Rx channels 16 6
Peak Tx Power ~1200W ~800W
A/D resolution 12 bits 12 bits
Min detectable signal -161 dBm -161 dBm
Noise Figure 5 dB 5 dB
Platform NASA P3 Twin Otter
System parameters
MCoRDS/I – Multichannel Coherent Radar Depth Sounder/Imager
*CReSIS. 2018. MCoRDS Data, Lawrence, Kansas, USA. Digital Media. http://data.cresis.ku.edu/
*Gogineni, S., J.-B. Yan, et al., "Bed topography of fast-flowing glaciers and fine-resolution mapping of internal layers", 26th IUGG General Assembly 2015, Prague, 06/22-07/2, 2015.

## Slide 10: Developing Artificial Intelligence algorithm for automated labeling
Label Seismic Data
Train Deep Networks using CNNs
Train Network
New Data
Trained Model
Semantic Segmented Data
Traditional approach – Did not work 
Deployed model :
Training :
Global accuracy of trained model <10%

## Slide 11: Why did our model fail?
Let’s understand the training data
High dynamic range results in :
Poor contrast in seismic image
Bedrock signal power very low
AI model cannot distinguish icesheet layers and bedrock
>200 dB dynamic range
Icesheets layers returns
Bedrock return

## Slide 12: How to detrend this data ?
Some techniques available in literature :
Curve fitting
  - Fit low order polynomial
  - Fit an exponential function
Predictive deconvolution
  - Inverse filtering
Result :
Loss in SNR of the bedrock return
Example :
Exponential curve fit
Original signal bed SNR = ~27 dB
Detrended signal bed SNR = ~20 dB

## Slide 13: Which technique to use ?
A wavelet is a rapidly decaying wave like oscillation with zero mean
Wavelets are best suited to localize frequency content in real world signals
Availability of a wide variety of wavelets is a key strength of wavelet analysis
Sine wave
Wavelet
Ans: Use wavelets analysis

## Slide 14: Introduction to Wavelet Multiresolution Analysis
Using DWT (Discrete Wavelet Transform) to analyze signals into progressively finer octave bands
90-180Hz
0-90 Hz
45-90 Hz
0-45 Hz
0-22 Hz
22-45Hz
Fs: 360 Hz
11-22 Hz
0-11 Hz
0-5 Hz
5 – 11 Hz

## Slide 15: Signal Preprocessing using Wavelet Multiresolution Analysis
Decompose signal into multiple resolutions using wavelets
Higher levels capture high frequency trends
Lower levels capture signal attenuation profile
Reconstruct the signal by combining higher levels and removing the lowest approx. level

## Slide 16: Signal Preprocessing using Wavelet Multiresolution Analysis
Results of multiresolution analysis
SNR of bedrock return is preserved as original signal ~27 dB
Used sym6 wavelet to preform the decomposition
Same wavelet decomposition method can be applied to all traces
Contrast of the seismic image improved

## Slide 17: Wavelets improve contrast for geologic boundaries
Results of multiresolution analysis

## Slide 18: After preprocessing, build deep learning model and deploy to nvidia GPUs
Train Model
Prepare Data
Deploy
Data Labeling
Deployment
Wavelet
Preprocessing
Model Visualization and Design
Tools:
Wavelet Toolbox
Deep Learning Toolbox
GPU Coder
Notes: Speaker Notes:
I will highlight some of the key features in MATLAB for the steps in the deep learning workflow that make it easier

## Slide 19: Developing Artificial Intelligence algorithm for automated labeling
Traditional approach did not work
Label Seismic Data
Train Deep Networks using CNNs
Train Network
New Data
Trained Model
Semantic Segmented Data
Deployed model :
Training :
Global accuracy of trained model < 10%

## Slide 20: Developing Artificial Intelligence algorithm for automated labeling
Signal Preprocessing with wavelets
Label Seismic Data
Train Deep Networks using CNNs
Train Network
Deployed model :
Training :
New Data
Trained Model
Semantic Segmented Data
Signal Preprocessing with wavelets
Global accuracy of trained model ~ 95%
New Wavelets based approach: AI model works 

## Slide 21: Overall result
Semantic Segmented Data
Confusion matrix plot for all pixels

## Slide 22: Summary of case study
Direct application of deep learning model is not useful for facies segmentation
Signal preprocessing is an important step to leverage the latest AI techniques for seismic interpretation, particularly at geologic boundaries
Overall SNR Improvement in signals : Multiresolution analysis decreases the dynamic range, helps uncover features in low SNR scenarios
Accuracy of 95% achieved
Improved features of icesheet layers and bed rock

## Slide 23: Paper presented at multiple conferences
AAPG ICE 2019, Buenos Aires
Geo Expo 2020 (link)
AAPG ACE 2020 (link - theme 7)
Poster presented at AAPG ICE 2019
More details and full presentation in following videos
Seismic Analysis with Wavelets and Deep Learning
Wavelets – A hidden gem for Artificial Intelligence in seismic interpretation

## Slide 24: We propose using the same workflow for parihaka seismic volume
We propose to apply the wavelet transform to all seismic data as a preprocessing technique
By improving the quality of the data for the deep learning algorithm, this methodology allows for the determination of layer boundaries, faults, and fractures. Thus, we can directly tackle one of the challenges of this hackathon
Finally, we intend to use GPU Coder to automatically generate CUDA code for deployment to NVIDIA GPUs